## Slide 1
FSR Training
Pillar 1 - Supplier Approval
2024
Notes: Welcome to Field Service Representative training. This will be the first of several training modules. Each section is relevant to the task that you will need to complete. This is a companion training to our Supplier Quality Assurance Field Service Representative Audit Guide. This particular training is focused on Supplier Approval Process. Any questions that arise from this training, please contact your SQA regional manager directly.

## Slide 2: SQA Field Representative Training Overview
Website Navigation
Regional Map
Common Acronyms
Types of Work Directives
Sample Work Directive
Section 1 - Supplier Approval Process
Quiz 1
Section 2 - Inspection Delegation
Frequently Missed Items
Common Questions
Quiz 2
Notes: The Training will consist of how to navigate the website www.gdls.com. The website contains various information you and the supplier will need to be familiar with. Our expectation is you will share this information with the supplier as needed. Also discussed will be the bullets listed on this slide. We will go into detail on each section. As mentioned previously, this is also meant to be a companion to the Supplier Quality Assurance Field Service Representative Audit Guide. Please be sure to review and become familiar with the information contained in the guide. There will a quiz at the end of each section to test your comprehension of the material found in the guide or mentioned in this training.

## Slide 3: GDLS Website – www.gdls.com
DO NOT BOOKMARK ANY PAGES
Notes: Navigate to the GDLS webpage www.gdls.com. To get to the quality information, click on Suppliers In the upper right hand corner. Then click on Quality. This has a lot of important information for you and the suppliers. As a reminder, do not bookmark these pages as security updates their protocol continuously and bookmarks may take you to obsolete revisions of the documents.

## Slide 4
GDLS Website – Regional Map
Notes: The regional map contains all the contact information for the SQA personnel. It is organized into regions and color coded for ease of matching the region to the proper regional manager. This is updated as needed and placed on the website. It also contains back up contact information in case your regional manager is unavailable. You may also email questions or concerns to sqa@gdls.com. This is manned by SQA and any questions, work, concerns, etc. will be reviewed and forwarded as necessary.

## Slide 5: Common Acronyms
ATGM | Anti Tank Guided Missile
CA | Corrective Action
CCR | Canada Change Request
CGD | Controlled Goods Directorate
CGP | Controlled Goods Program
COB | Close of Business
COC | Certificate of Conformance
COTS | Commercial Off The Shelf
CP | Control Plan
CV | Commander's Vehicle
CT | Control Test
DCMA | Defense Contract Management Agency
DFARS | Defense Federal Acquisition Regulation Supplement
DOD | Department of Defense
ESV | Engineer Squad Vehicle
FAA | First Article Approval
FAI | First Article Inspection
FAR | Federal Acquisition Regulation
FAT | First Article Test
FMEA | Failure Mode and Effects Analysis
FPI | First Piece Inspection
FSR | Field Service Representative
FSV | Fire Support Vehicle
IAW | In Accordance With
ICV | Infantry Carrier Vehicle
ITAR | International Traffic in Arms Regulations
IUID | Item Unique Identification
LAV | Light Armor Vehicle
MC-B | 120mm Mounted Mortar Carrier
MEV | Medical Evacuation Vehicle
MGS | Mobile Gun System
MOD | Ministry of Defense
MRAP | Mine Resistant Ambush Protected
MRB | Material Review Board
MRI | Machine Readable Information
NBCRV | Nuclear Biological Chemical Reconnaissance Vehicle
NC | Non-Conformance
NCG | No Change Clause
OCM | Original Component Manufacturer
OD | Ordering Data
OEM | Original Equipment Manufacturer
QAP | Quality Assurance Provisions
QAR | Quality Assurance Requirements
QE&T | Quality Engineering & Test
QPL | Qualified Parts List
PO | Purchase Order
RCCA | Root Cause and Corrective Action
RV | Reconnaissance Vehicle
RTS | Return To Supplier
SCR | Sterling Heights (U.S.) Change Request
SEP | System Enhancement Package
SPC | Statistical Process Control
SPN | Service Problem Notice
SPT | Ship Prior to Test
SQAP | Supplemental Quality Assurance Provisions
SQMR | Supplier Quality Material Report
TRA | Temporary Release Authorization
UAI | Use As Is
UII | Unique Item Identifier
Notes: In the course of doing business with GDLS you make come across a variety of acronyms. This is a listing of some you may encounter.

## Slide 6: Types of Work Directives
VQSA – Vendor Quality System Audit – is used when doing a on-site system audit
VMIN – Verify Minimum Quality System Audit – used for on-site system audit for Distributor
VIDA – Verify Inspection Delegation Stamp Audit – is used for Stamp Delegation audit
VFP – Verify First Article Inspection – used for QY-11 FAI
VFPD – Verify First Article Inspection Desktop - is used for FAI via desktop
VLFP – Verify London First Piece Inspection – is used for QY-12 clause FPI for Canadian PO only
VLFPD - Verify London First Piece Inspection – is used for QY-12 clause FPI for Canadian PO only desktop
VSV – Verify Source Inspection – is used for source inspections (QY-11, QY-12, EQD2A)
VSVD – Verify Source Inspection Desktop – is used for source inspection via desktop
VGL – Verify General Log – is used for general visit
Notes: There are a variety of audit types you may be assigned while working for GDLS. This is a list of the common audit types. These types of work directives guide you to the scope of the audit. We will focus only on Supplier Approval Work Directives in this section. For example, the first one VQSA is a complete quality system audit. This is assigned to manufacturing suppliers. These types of suppliers are the most important suppliers, as they are higher risk. The VMIN is a system audit for distributors. They are non-value added suppliers. The VIDA is performed only to those supplier who have inspection delegation stamps.

## Slide 7: Sample Work Directive
Sample Work Directive as received from GDLS SQA Regional Manager
Audit Type determines work needed to be completed
Sequence Number is found at the top of the page in the middle. This is used as an identifier for your time card and tracking for GDLS.
Specific instructions for audit type
Notes: All three of the audit types discussed on the previous slide will look vary similar, but will require different forms to be completed and returned to your SQA Regional Manager. All audits launched are your work directives and will contain sequence numbers used for tracking purposes. The sequence number is found at the top of the page in the middle of the form. This is used as an identifier for your time card and tracking for GDLS. It contains the supplier you are to visit, their contact information, current quality scores and your GDLS SQA Regional Manager. However most importantly it contains instructions that you are to follow. These are found in the Instruction section of the work directive and generally have additional forms that need to be completed and returned with your work directive. Once audit is complete, Record mileage, travel hours, and actual on-site hours. Please log this information in an area that can be easily recorded and legible. Any additional costs must also be labeled and recorded (e.g. Tolls, hotel …). Any overtime or overnight travel must be approved by the Regional Manager prior to departing for the audit. As mentioned previously, the sequence number is used for tracking purposes and the contract house you work for uses the sequence number when billing GDLS for your services. It is very important to ensure you use the correct sequence number on your time card. The main issues we have with billing is the incorrect reporting of the sequence number due to typo’s, or mixed numbers or they are not legible. If a work directive is not used (no charges made) please return it to your Regional Manager and let them know this. If any work was done on it, please record the time and return to your GDLS SQA RM.

## Slide 8: Supplier Quality Assurance
Supplier Approval
Quality Systems Audit
Active Supplier List
Production Part Approval
First Article Inspection
Technical Data Package
Quality Performance
Quality Rating
Variance
Corrective Action
Quality Clause (QY 11, 12, 14, 15)
Inspection Delegation Program
Supplier Approval
Notes: At a high level glance, this slide depicts the scope and responsibilities of GDLS Supplier Quality Assurance. As stated before we are focusing only on supplier approval and inspection delegation in this section. Inspection Delegation is a method of further management and trust with the supplier. Only suppliers that are well trained should have stamps, therefore it is important that the suppliers that hold stamps are highly informed of GDLS processes, expectations and performance goals. Having stamps is a privilege that can be removed for cause. For example, misuse of stamps, poor performance, etc.

## Slide 9: Section 1: Supplier Approval Process – Quality System Audit
All production supplier’s MUST have a quality system audit performed – VQSA or VMIN
  VQSA is used for all production suppliers, except distributors
  VMIN is used for distributors
A supplier categorized as commercial only has PO’s for commercial product. No scheduled system audit will be required
ISO9001, IATF 16949, AS9100 may be accepted in lieu of completing the checklist questions. The Certification MUST match the supplier location being audited. Verify expiration date is current.
Supplier Approval
Notes: There are two reasons GDLS does supplier approval audits: a new supplier or revalidation of current suppliers. For a new supplier, SQA will receive a request from Supply Chain Management Buyer to complete a quality system audit. It will either be a VQSA or VMIN. If the supplier is a commercial supplier no audit is required. A commercial supplier is a supplier of product meeting the producer’s own standards and does not differ from the product offered for sale in the commercial market. We do accept quality management certification such as ISO 9001, AS9100, etc. in lieu of completing the VQSA/VMIN checklist. All Suppliers must be approved by GDLS, regardless of approvals by customers or other entities. Approvals are site specific and each manufacturing or distribution site will require an individual approval (sites that manufacture or where the FAI/Source occur shall be audited). PO sites or head quarters are not necessary to be audited. When ISO certs, etc. are accepted, be sure that the address listed on the certification matches the audit location.
-Suppliers shall develop, document, implement and maintain a quality system providing the highest degree of confidence that the material and services will conform to contract requirements.
-GDLS requires suppliers to provide immediate notification in the event that any certifications have been lost and any notifications of significant changes within the supplier’s organization (e.g., changes related to address, ownership, key management, scope of operations).
-The supplier's quality system shall provide for control of purchases and services from sub-contractors to include, but not limited to, conveyance of applicable contract and technical requirements and a method of assessing sub-contractor’s capability and performance to contract/technical requirements
-.

## Slide 10: Supplier Approval Process – Quality System Audit
All audit types must have:
  Suppliers’ quality contact information verified – name, address, phone, email, etc.
  Review of the suppliers’ 12 month quality score. If it is below 98%, an on-site audit must be done regardless of QMS certification.
  A Clearly stated pass or fail.
    If failed, a report containing the findings must be noted on the audit.
    List each non-conformance in the auditor's remarks area. BE SPECIFIC
    Be sure to notify the Regional Manager as soon as possible of failure.
  A copy left with supplier and sent to the SQA Regional Manager.
Supplier Approval
Notes: After you receive the work directive from your GDLS regional manager contact the supplier using the information provided on the work directive. If you have any issues contacting the supplier, please let the regional manager know. After contacting the supplier, schedule the on-site audit, if applicable. During the audit, verify the supplier quality contact information is accurate. Be sure to follow the instructions outlined in the work directive and any additional instructions your regional manager may have communicated. At any point if you have issues, contact your regional manager. Be sure to be specific when writing nonconformances and findings. After completing the audit, leave a copy with the supplier and send results to your GDLS SQA regional manager. The following slides will go into detail on how to complete the audits.

## Slide 11: VQSA – Vendor Quality System Audit
Follow the instructions with the VQSA
All fields to be filled in. For any negative responses, the auditor must clearly explain why there is a NO response. For yes responses, you MUST have evidence detailed on the VQSA.
Make sure you are using valid example of compliance and notate it in the Audit Evidence column or in the Observations/Notes section for each question.
Spaces that have N/A blacked out must answer yes or no. These questions cannot be N/A.
Supplier Approval
Notes: The VQSA is based off the ISO 9001 quality system standard. The VQSA audit form will be attached in the email with your work directive from your GDLS regional manager. The work directive will have the supplier’s quality rating. If the score is below 98%, an onsite audit is recommended to be done and the QSA filled in even if they have a quality management certification. If going onsite, ask the supplier to prefill out the VQSA audit prior to your on-site visit, so it is ready for you when you arrive. It is the Field Service Representative’s responsibility to review responses and report the accurate situation of the supplier’s quality system even if the supplier pre-filled out the form. You are the eyes and ears of GDLS. There is an instruction section on the VQSA forms that is available for direction, however, your regional manager should be contacted if you have questions or concerns. The forms provide room for identification of evidence used to show compliance to each question. All the fields need to have an answer or if there is no response, clearly explain why there is no response. On the form there are some N/A spaces that are blacked out which means the supplier must answer yes or no. Be descriptive as possible when recording answers of evidence used. The last column on the form shows example of evidence that could be used to show compliance. These are just examples of evidence. Other items can be used as long as they are applicable and show compliance to question asked.
If the supplier is a current GDLS supplier, every month, GDLS sends out Supplier Performance History to the supplier. This is covered in a later slide, but in is important to note that a review of GDLS nonconformances need to be made and review the suppliers reactions to these nonconformances, especially if their quality score is low.

## Slide 12: VMIN – Vendor Minimum Quality System Audit
Verify that the supplier (distributor) does not conduct any value added to the parts supplied.
  Value added examples are but not limited to: adding labels, coatings, kits, modifications to part
  Special processes should not be applicable for VMIN. If they are done, contact Regional Manager for further direction.
Complete the audit checklist questions.
  The work directive contains the VMIN questions
Please print and sign your name, apply your stamp in this area as well as the date the audit was completed AND place the PASS/FAIL status. (an electronic signature and stamp is permissible)
Please report results/comments and information related to the audit that needs to be communicated to GDLS. List any non-conformances in the audits remarks area. BE SPECIFIC
Supplier Approval
Notes: The VMIN work directive is a quality system assessment used for distributors. If the supplier conducts any value added processes (assembly, kitting, inspection,…) then a VQSA must be done in place of a VMIN. Contact your Regional Manager to have the VMIN cancelled and to get the VQSA audit assigned and a new work directive sent to you.

## Slide 13: FYI
The work directives no longer contain Part Numbers, shipment history or nonconformances written against supplier
  VQSA, VMIN, Special Process Audits or VIDA
Refer to Monthly Performance data sent from GDLS to suppliers for this information.
  Plan ahead and send Audit forms for the supplier to review/prepare/complete/find evidence for prior to audit
    Smoother more efficient audit completion
    Nonconformance history is sent to the suppliers on a monthly basis. When performing audits, a review the nc history is to be completed
Notes: Due to increasing security measures, to safeguard data, the work directives do not contain part numbers, shipment history, or non-conformance history. The suppliers receive a monthly supplier scorecard with this information you can review at time of audit. Plan ahead and have the suppliers prefill out the audit paperwork for a smoother, more efficient on-site audit.

## Slide 14: Special Process Audits
The following Special Process Audits need to be completed at time of system audit:
  V701/702 – High Strength Fasteners
  V818 – Approved Independent Distributor (trusted supplier)
  V820 – ASTM A514 Material Supplier
  These all require a specific checklist. This form must be completed. No blanks permissible.
  If you did not receive, please ask for it from your regional SQA mgr or sqa@gdls.com
  All other special processes are validated during FAI.
Supplier Approval
Notes: Special processes (painting, plating, heat treating, welding, etc.) are a vital component of manufacturing and can introduce vulnerability on the overall process. If special processes are involved in the production of the supplied product, Nadcap Accreditation is accepted for the special process. Soldering must meet the appropriate IPC standard. The supplier will provide all documentation indicating accreditation upon request or if not accredited, compliance to specification during FAI/FPI. GDLS will officially do 3 special process audits as a must: High Strength Fasteners, Approved Independent Distributor and ASTM A514 Supplier. These 3 special process audits have their own type of audit and will be assigned as another work directive and it is to be done at the same time as the system audit. Further detail on the 3 special process audits are on the following slides, however, any other special process audit can be done at the direction / request of the GDLS SQA regional manager and only if they add it as an instruction when assigning the audit to you. As a normal process, special processes shall be validated during FAI/FPI.

## Slide 15: V701/702 - High Strength Fasteners
Review the Purchase Order for specific Quality Clauses relative to High Strength Fasteners such as:
  QL-22 Screws/Fasteners,
  QP-41 Traceability MS Fasteners (CAD),
  QP-43 Traceability - MS Fasteners (Zinc),
  QP-44 North American High Strength Fasteners including Form 4496 for GDLS - Canada.
The clauses require procurement from manufacturers approved by GDLS. Contact SQA Regional Manager for list or sqa@gdls.com
All Fasteners procured for US programs must be supplied by a V701 supplier
Non‐US programs, fasteners may be procured from a V701 or V702 supplier.
Actual test results such as Physical, Chemical and Plating requirements must be provided upon request.
Supplier Approval
Notes: The first required Special Process Audit to cover is High strength fasteners (Grade 5 and 8 and metric classes 8.8, 9.8, 10.9, and 12.9). These fasteners are used in specific assembly applications for various reasons. When the application is critical as determined by engineering, the purchase order will contain a unique requirement indicating so (Quality Clauses QL-22, QP-41, QP-43 & QP-44). The Quality Clauses are to be followed. All quality clauses require the fastener to be purchased from an approved GDLS MFG. The list of approved manufacturers may be requested from GDLS. There are 2 lists. One for suppliers procured for US programs (V701) and one for Non-US programs (V702). In all cases, the supplier must have evidence of compliance. A separate V701/702 special process audit is assigned to suppliers that manufacture High Strength Fasteners that are used on GDLS products. In the case of assemblies, if a high strength fastener are used, the supplier of the assembly is to use a GDLS approved manufacture for the fasteners. When a V701/702 audit is assigned to you, a work directive will be sent to you. The work directive will contain a sequence number, the supplier, and contact information. Please contact the supplier and complete the V701/702 forms. Please complete the assigned audit utilizing the form accompanying the audit, sign, stamp and return the audit to the GDLS SQA Regional Manager.. As a talking point, stress that it is recommended that the FSR ask for test results periodically to validate compliance

## Slide 16: V701/702 - High Strength Fasteners- additional information
Supplier Approval
High Strength Fastener Guidelines:
Supplier must be on the V701/702 approved list
Must be marked by the manufacturer with the specified grade identification symbol in accordance with the applicable standard.
The heads of such hardware must bear the manufacturer's head logo.
Notes: GDLS has a Standard Practice that specifies ordering, procuring and testing of these types of fasteners for use in GDLS products. V701 must only be manufactured in the US per the DFAR for specialty metals. The Heads of fasteners will be marked with a manufacturer symbol per the applicable standard. There are websites available that will identify the manufacturers symbol. V701/V702 lists should be at supplier’s location or available by contacting your GDLS regional manager.

## Slide 17: V818 – Approved Independent Distributor (trusted supplier)
Supplier Approval
Counterfeit Avoidance/Mitigation Requirements for Electronic Components & Assemblies
The supplier must be GDLS approved
  V818 audit used to place on approval list
    Regional Manager will provide you;
      V818 work directive
      V818 Checklist
Complete the V818 checklist and return to your regional manager with your mileage/time.
Notes: V818 audits are used to approve a supplier as an independent broker for electronic components. The work directive will contain a V818 checklist. Please complete all questions with detailed answers and return to regional manager with your time/mileage. Please refer to FSR audit guide and the PQA-3000 for further details or contact your regional manager with questions.

## Slide 18: V820 – ASTM A514 Material Supplier
First Time Audit
Receive work directive and audit checklist from regional manager
Complete checklist
  Some questions may be N/A for first time audit
Send completed audit to Regional Manager with time/mileage
Surveillance Audit
Done every 2 years
Please note that the surveillance audit has additional questions and requires a review of:
  Valid approval letter
  Cutting Log (SCM-037)
    Validate 3 material certifications of prior shipments
Supplier Approval
Notes: V820 Audit is used for suppliers, including distributors, providing ASTM A514 steel 1.25” thick or greater. Suppliers must be on the approval list to provide A514 material. It is designated on the supplier’s PO with QK19 quality Clause. Your SQA regional manager will provide you with the work directive and A514 audit checklist to be completed at time of audit. Please note that there are differences between a first time audit and a surveillance audit. During a first time audit, some of the questions may not be applicable. Please refer to your FSR audit guide or PQA-3000 for further directions or contact your regional manager.

## Slide 19: Quiz 1 – Supplier Approval Process
Supplier Approval
What special process audit is needed for A514 material?
  V717
  V820
  V701
  V818
  2. A VQSA or VMIN is required for commercial suppliers.
    a) True
    b) False
    3. What information are you looking for on the QMS certification. Circle all that apply.
      Expiration date
      Location you are auditing
      Quality managers name
      Scope of certification
Notes: Please take the next few minutes to complete Quiz 1. Open the attachment that came with your work directive and highlight your answers. When complete send with your work directive to your Regional Manager along with your recorded time.

## Slide 20: Section 2: Inspection Delegation (QJ-21)
There are NO receiving inspectors in any of our GDLS Receiving Locations.
Inspection Delegation (ID)
  GDLS certified supplier program
  PO quality clause QJ-21
  GDLS stamp unique to individual(s) supplier quality personnel
    If stamp holder is no longer with company, the stamp must be collected and returned to regional manager
    ID Stamp holders will be audited every 2 years or as directed by GDLS SQA Regional manager for compliance using the VIDA audit.
Supplier Approval
Notes: Section 2 of this training covers Inspection Delegation. Inspection delegation is GDLS certified supplier program. GDLS is delegating the authority to accept parts on our behalf after the supplier has completed inspection delegation training and received a GDLS stamp. Each part number shipped under the ID program must have a GDLS approved FAI prior to the Supplier’s Inspection Delegate stamping off GDLS shipments. Inactive stamps must be collected and returned to your GDLS regional manager. The VIDA audit is done approx. every 2 years to verify compliance on suppliers who have stamp holders.

## Slide 21: VIDA – Verify Inspection Delegation Audit
Coordinate with the supplier so ALL stamp holders can be present.
Review questions and have supplier prepare information in advance to help expedite as well as prepare the supplier for this audit.
Verify the company address, quality assurance point of contact name, Email address, phone number. List the current quality assurance point of contact's email address.
Please verify you have the correct revision level of the SQ-905 form before conducting the audit.
Verify supplier is familiar with packaging requirements.
If there are any stamp numbers that are incorrect you should contact your GDLS Regional Manager
Please print and sign your name, apply your stamp as well as the date the audit was completed. You will also write that the audit PASSED or FAILED
Supplier Approval
Notes: When conducting a VIDA audit the Quality Representative and all stamp holders must be present for the audit. If stamp holders are on vacation, sick, on a different shift, etc. you may need to wait to schedule with the supplier so they can all be present. To help expedite the on-site visit have the supplier prepare information in advance for questions 9, 12, 13 and 14. Performance history is sent to the supplier on a monthly basis and will need to be available for VIDA audit. For question 12, randomly select shipments and review the documentation was completed correctly. Complete the VIDA checklist questions and return to your GDLS regional manager.

## Slide 22: Inspection Delegation (QJ-21)
STAMP RULES:
  This stamp will always be kept under personal control and secured from unauthorized use (stamps are not borrowed or loaned).
  Assignee must have independent authority to accept or reject product shipment(s). Must also be unencumbered from contacting their SQA Regional Manager with any questions or concerns.
  Stamp use is only for its intended purpose, the review of GDLS product and documentation (a written/typed stamp number is not valid).
  Immediately notify your GDLS Regional Manager if this stamp is lost, stolen, or if it cannot be used because of damage or wear.
  Immediately notify your GDLS Regional Manager if you suspect any misuse of this stamp.
  The stamp impression must be affixed to all copies of the shipping document only when compliance to the Purchase Order and TDP are fully met. This is the only form of product acceptance.
Supplier Approval
Notes: These are the Inspection Delegation stamp rules the supplier must follow. Please be familiar with them.

## Slide 23: Frequently Missed Items
Supplier Approval
From VQSA, question 9, Are stamp controls established preventing unauthorized use?
Supplier missed source changes from one shipment to next(ignoring configuration control fka no change clause) and used delegate stamp to ship.
GDLS requirements are not being properly flowed down to sub-tier suppliers.
When FSR is completing VIDA audit, question 5, the method of flow down is not being documented.
All stamp holders not present or accounted for during VIDA audits
Supporting evidence notated for all system audits
Notes: When conducting audits these are some items that are commonly missed. Please review the list and make yourself familiar with the requirements. You are the eyes and ears for GDLS and we depend on you.

## Slide 24: Common Questions
Supplier Approval
Common Questions | Answers
Who do I contact if I have issues with my timecard? | Timecard questions should be directed to your contract house
What do I do if I have issues with my contract house? | Please direct concerns with your contract house. If you are unable to get satisfactory assistance and it is impacting how you perform your support to GDLS, please send concerns to sqa@gdls.com or contact your SQA Regional Manager (RM)
What do I do if I have conflict with a supplier that I visit on behalf of GDLS? | Please immediately contact GDLS to discuss with your RM
Notes: These are a few common questions with answers that may arise while working for GDLS. When in doubt, please contact your regional manager for clarification.

## Slide 25: Quiz 2 – Inspection Delegation
Supplier Approval
When are VIDA audits required?
  Every year
  Every 3 years
  When a delegate retires
  When supplier is delegated
  A delegate stamp can be transferred/used by different employees.
    a) True
    b) False
    3. How is Configuration Control (fka No Change Clause) validated?
      Review previous FAI packages
      Review sub-tier supplier PO
      Review shipper
      Review gage calibration
      Stamp holders do not all need to be present during VIDA audit.
        True
        False
Notes: Please take the next few minutes to complete Quiz 2. Open the attachment that came with your work directive and highlight your answers. When complete send with your work directive to your Regional Manager along with your recorded time.

## Slide 26: Pillar 1 - Supplier Approval - COMPLETED
Supplier Approval
Notes: Congratulations you have completed the first training module. Please contact your regional manager for any additional questions or concerns.