## Slide 1: Inspection Delegation Program 2026
Next Slide

## Slide 2
Training Overview
Acronyms
Training Purpose
Inspection Delegation Program Overview
Delegate Authority & Accountability
Contract Review
Sample Purchase Orders
Contract Issues & Escalation
Configuration Control
Data Retention
Lot Sampling
AQL C=0 Lot Sampling Chart
Supplier ID Lot Verification Checklist
Inspection of Part Marking
Part Marking Requirements
Technical Data Package Review
Technical Data Package Common Rejections
Certificate of Conformance
Material Certifications
Discovery of Nonconforming Product
Know the Difference – Rework vs Repair
Final Shipment Authorization
Vendor Inspection Delegation Audit
Inspection Delegate Responsibilities
Inspection Delegate Stamp Rules
Unwavering Commitment to Quality
Thank you
Next Slide
Previous Slide
Notes: Welcome to the GDLS Inspection Delegation Program training. Please use the audio button to pause and play the script as needed. Today, we’ll cover the key responsibilities and requirements for Inspection Delegates, including contract review, configuration control, lot sampling, part marking, and data retention. We’ll also discuss how to handle nonconforming products, the difference between rework and repair, and the process for final shipment authorization. Our unwavering commitment to quality ensures that every product meets GDLS standards and supports the safety of those who rely on our work. Thank you for your dedication and attention to detail.

## Slide 3
Acronyms
AQL – Acceptable Quality Level
BOM – Bill of Material
CAPA – Corrective Actions & Preventive Actions
CM – Configuration Management
CPR – Canadian Problem Report
COC – Certificate of Conformance
COTS – Commercial off the Shelf
FAI – First Article Inspection
FAIR – First Article Inspection Report
NCH – Non-Conforming Hardware
OD – Ordering Data
PO – Purchase Order
PR – Problem Report
QAR - Quality Assurance Requirements
QAP- Quality Assurance Provisions
RCCA – Root Cause & Corrective Actions
SCD – Source Controlled Drawing
SPR – Sterling Heights Problem Report
TDP – Technical Data Package
VICD –Vendor Item Controlled Drawing
VIDA – Vendor Inspection Delegation Audit
Next Slide
Previous Slide

## Slide 4
Delegated inspection authority shifts execution, not responsibility
Most quality escapes occur after First Article Inspection (FAI)
This training focuses on preventing shipment(s) of nonconforming products
Delegates play a critical role in customer protection
This training will define the responsibilities of the supplier’s GDLS inspection delegate(s).
Training Purpose
Next Slide
Previous Slide
Notes: This training exists because data shows that once FAI is approved, defects are still escaping and making it to our GDLS Assembly Plants. These are not FAI failures - they are manufacturing and inspection control failures during production. Delegation does not reduce requirements; it increases responsibility. The goal here is to prevent escapes before shipment(s), not react after the fact.

## Slide 5
Inspection Delegation Program
>98% 12 month
-Approved status
Documented process detailing:
-Supplier responsibility/Scope of delegation
-List of Delegates
-Training of Delegates
-Product training
Supplier ensure on the job training:
-Product knowledge
-Specific training required to fulfill delegation expectations
-GDLS must provide delegate training
Once validation of supplier's systems, training and knowledge is complete, a Quiz is administered.
Upon passing a personal stamp is assigned
Verification every year to ensure compliance of program
-VIDA audit (Stamp) done yearly
-QSA (Quality System Audit) done every 3 years
-QA responsibility
-Product Knowledge
-Access to TDP
-QJ21 form
No Receiving Inspection – Parts go directly to Plant Production and/or to GDLS Customers for use in the field for repairs and upgrades
Next Slide
Previous Slide
Notes: GDLS has an Inspection Delegation program. The PQA-3000 details the requirements of the program. This slide is a very high-level overview of activities for the ID program. To become a participant the following steps shall be taken;
A Suitable candidate is identified per the criteria defined in the Inspection Delegation Guide. The candidate must apply for an ID stamp using the QJ21 worksheet found at www.gdls.com. The QJ21 worksheet also contains the steps to be followed prior to issuance of individual stamp. The Supplier is to develop a process to internally control issued stamps and training of identified delegate(s).All requirements in the PQA-3000 are followed.
Potential delegate(s) to attend GDLS Stamp training. Once stamp training is completed and any other necessary activities, the delegate(s) will take a Quiz, and a stamp may be issued.
There is no receiving inspection – suppliers are expected to supply conforming parts. All prints should be reviewed upon acceptance of the purchase order. If any questions arise, address them immediately with your buyer.
Quality system audits are scheduled every 3 years. The Inspection Delegation stamp audit, will occur every year either onsite or as a self assessment. This process has specific duties that each participant must follow. Take a moment to review the flow, task, activities and duties. Direct any questions you have of this process to your GDLS SQA Regional Manager.

## Slide 6
Delegate Authority & Accountability
Inspection delegates approve product on behalf of the GDLS
Stamped packing slips by GDLS Inspection Delegate equals GDLS acceptance
    No receiving inspection at GDLS plants
Improper release may result in:
    Escapes to assembly
    Cost and schedule impacts
        Parts return at supplier cost
  Suspension or removal of Inspection delegation authority (removing GDLS stamps)
Next Slide
Previous Slide
Notes: Delegation authority is not to be taken lightly. A delegate stamp takes the place of a receiving inspection at the GDLS plant. When a shipment arrives from a supplier the Material Department accepts or rejects the lot by reviewing the packing slips and verifying the presence of the GDLS Inspection Delegate stamp. Improper releases may result in impacts to cost and schedule at the GDLS plants. Delegation authority is conditional and performance based. SQA reserves the right to suspend or remove the supplier from the Inspection Delegation program if deemed necessary.

## Slide 7
Contract Review: Required First Step
Review PO and technical data package upon receipt of order from GDLS
Review and Confirm:
    Ensure the revision levels of the technical data package match what is listed on the PO
    Applicable drawings and specifications
    Flow-down requirements
    Inspection, marking, and traceability requirements
    Quality Clause requirements
        QAR/QAP
        Ordering Data
Next Slide
Previous Slide
Notes: The Technical Data Package contains all the information needed to prove the part is compliant to GDLS requirements. The delegated stamp holder is responsible to assure all GDLS Purchase order & TDP requirements are satisfied. This includes any requirements that may need to be flowed down to sub-tier suppliers. Please ensure no quality assurance requirements, quality assurance provisions or ordering data has been overlooked during the contract review. When presenting a part to a GDLS representative, all the applicable items are required to be present to gain GDLS approval. Many escapes trace back to missed notes, outdated revisions, or misunderstood requirements. When in doubt you should contact your GDLS Buyer & SQA Regional Manager for clarification.

## Slide 8
Contract Review: Sample PO - US
GDLS U.S. PO
PO’s for the US start with 4
Location of Quality Clause under the line item number
Next Slide
Previous Slide
Notes: The GDLS US Purchase Orders will start with the number 4 as part of the identifier. The part revision level is listed below the part number, and the quality clauses are listed below the revision level in item text. Please review the above visual slide as an example.

## Slide 9
Contract Review: Sample PO - London
Canadian PO’s start with a 3 as a number
The Drawing Rev and quality clauses are part of header of line
GDLS CANADA PO
Next Slide
Previous Slide
Notes: GDLS has 2 business units: GDLS-Canada and GDLS USA. Each Purchase order looks slightly different. The GDLS Canada Purchase orders will start with the number 3 as part of the identifier. Also, at the top Canada will be under the General Dynamics logo. Another main difference is that the revision level is in revision box and the quality clauses are listed in the QA Clause box on same line item as the part number being ordered. The GDLS buyer contact information is available in the Purchase order header.

## Slide 10
Contract Issues & Escalation
Notify your GDLS Buyer immediately if requirements are:
    Unclear
    Missing information
    Conflicting
    Outside your manufacturing and inspection capabilities
    DO NOT interpret requirements independently – consult with your GDLS buyer or SQA Regional Manager for direction
Next Slide
Previous Slide
Notes: Delegates are not authorized to interpret or waive requirements. If any requirements are unclear, missing, conflicting or outside of your manufacturing and inspection capabilities, please contact your GDLS buyer immediately. Do not try to interpret requirements independently. If something does not make sense, the correct action is escalation - not assumption. Consult your buyer or SQA regional manager for direction. If you receive a U.S. or Canadian purchase order and there aren’t any quality clauses listed on our PO there is an error and your GDLS Buyer must be notified to correct the PO. Do not ship parts to GDLS with a PO that does not have quality clauses. Shipping without clarification transfers risk directly to GDLS and our customers.

## Slide 11
Configuration Control: Purpose
Contractual Requirement found in PO Terms and Conditions
Formerly known as the “No Change Clause”
FAI approval freezes the design and processes used to make production parts
“No change” applies unless formally approved from a FAI or delta FAI.
Applies to:
  Design, Materials, Manufacturing process, Manufacturing location, Assembly process, Sub-tier suppliers, and Source of supply
Next Slide
Previous Slide
Notes: Configuration Control is a very important supplier function found within the supplier Purchase order terms and conditions. Suppliers must notify GDLS of any changes in design, materials, manufacturing location, manufacturing process, assembly processes, or source of supply. Likewise, if a sub-tier supplier has changes in the same manner as above, notification to GDLS must be made to your GDLS buyer. The approved FAI represents a frozen configuration. Any change, intentional or not, will invalidate the FAI approval and a delta FAI would be required.

## Slide 12
Configuration Control – PO Terms & Conditions
Configuration Control (Changes) fka No Change Clause
  Applicable to all suppliers and must be flowed down to all Sub-tier Suppliers
  ALL changes per GDLS Terms and Conditions require written approval from your GDLS Buyer
  Will require full or partial FAI after receiving written approval from your GDLS Buyer
Next Slide
Previous Slide
Notes: If a change request is needed, please ensure it is communicated to your GDLS buyer. The change must be approved in written form from your GDLS buyer and will require at minimum a partial FAI after that approval is received.

## Slide 13
Configuration Control - Design Changes
Includes, but not limited to:
  Drawing changes
    This includes supplier designed parts (source control and vendor item control drawings)
  Specification changes
  Supplier-initiated design modifications
Requires customer approval – Per GDLS Terms and Conditions any changes require written approval from your GDLS Buyer.
Will require full or partial FAI after receiving written approval from your GDLS Buyer
Next Slide
Previous Slide
Notes: This includes supplier designed parts such as source control and vendor item control drawings. Specification and supplier-initiated design modifications are included and require written approval from your GDLS buyer. Even small design changes can affect fit, function, or durability. Verbal approvals or “same-as” assumptions are not acceptable. We have had issues resulting is sales stoppage as far down the supply chain as tier 5 design changes.

## Slide 14
Configuration Control - Process Changes
Includes, but not limited to:
  Machining Center changes – (e.g. moving location of machines, new machinery, etc.)
  Tooling Changes
  Inspection method changes
  Sequence or routing changes
“Equivalent” processes still require approval
Supplier’s must qualify processes internally to ensure they meet contractual requirements
Requires customer approval – Per GDLS Terms and Conditions any changes require written approval from your GDLS Buyer.
Will require full or partial FAI after receiving written approval from your GDLS Buyer
Next Slide
Previous Slide
Notes: Process changes require written approval from your GDLS buyer. Some examples included but are not limited to the following: Machine center changes, tooling changes, inspection method changes and sequence or routing changes. Supplier’s must qualify processes internally to ensure they meet contractual requirements. If the process used today is not the same as the approved FAI process, then a change has occurred and you must contact your GDLS Buyer and SQA for the next actions. We have had issues resulting is sales stoppage as far down the supply chain as tier 3 for unapproved process changes.

## Slide 15
Configuration Control - Sub-Tier Supplier Changes
Includes, but not limited to:
  Material suppliers
  Special processors
  Outside manufacturing suppliers
  Metrology Labs
  Applies to all tier levels
Sub-tier changes require approval
Certifications must be traceable to approved sources
Requires customer approval – Per GDLS Terms and Conditions any changes require written approval from your GDLS Buyer.
Will require full or partial FAI after receiving written approval from your GDLS Buyer
Next Slide
Previous Slide
Notes: All sub-tier supplier changes require written approval from your GDLS buyer. These include but are not limited to: Material suppliers, special processors, outside manufacturing suppliers, metrology labs and all other tier level suppliers. Certifications must be traceable to approved sources. Sub-tier control is a high-risk area. Delegates must confirm that the approved suppliers were used and have supporting documentation. Flow of all GDLS requirements is the responsibility of the supplier. Sub-tier suppliers at every level should understand these requirements.

## Slide 16
Data Retention
Retain inspection, testing and lot sampling records per 84-005-0807 PO terms and conditions section 6
Data may be required for activities such as:
  Field failures
  Non-conformances found after delivery to GDLS
  Root cause analysis
  Regulatory and contractual compliance
Next Slide
Previous Slide
Notes: GDLS requires inspection, testing and lot sampling records to be retained per 84-005-0807 terms and conditions section 6. This data may be used for field failures, non-conformance escapes, root cause analysis and regulatory and contractual compliance. If data does not exist, the inspection effectively did not happen. Retention protects both the supplier and the customer.

## Slide 17
Lot Sampling – Lot Definition
A lot consists of parts that includes, but not limited to:
  Same part number
  Same revision
  Same process
  Same time frame
  Same machining center
  Same assembly line
Improper lot definition invalidates sampling
Next Slide
Previous Slide
Notes: Improper lot definition invalidates sampling. A lot consists of the same part number, revision, process, time frame, machining center and assembly line. Lot Sampling only works when the lot is uniform and consistent. Mixing parts from different lots hides defects and increases escape risk.

## Slide 18
Lot Sampling - Sampling vs 100% Inspection
Some requirements may mandate 100% inspection
Lot sampling is required per quality clause QG5 – C=0 Sampling Plan
Selection of samples from the lot shall be done at random
VICD parts purchased from the recommended source of supplier will adhere to their manufacturers sampling plans
COTS parts will have lot sampling performed to manufacturers lot sampling standard
Additional lot sampling may be required based on:
  Quality issues
  Process capability
  Historical performance
  QAR/QAP requirements
  Regional Manager directed
Next Slide
Previous Slide
Notes: Lot sampling and 100% inspection are different. Although some requirements may mandate 100% inspection, almost all purchase orders will require lot sampling per quality clause QG5. Vendor item control and commercial parts will have lot sampling performed to the manufactures lot sampling standard. SQA reserves the right to require additional lot sampling based on quality issues, process capabilities, quality assurance provisions and requirements.

## Slide 19
Lot Sampling - AQL Fundamentals
AQL does not permit known defects
GDLS uses C = 0
  Suppliers will be required to institute an AQL of 2.5 for the first five (5) production lots produced. If there is no defect(s) found after the first five (5) lots produced suppliers may ease the AQL to 4.0.
  Maximum allowed AQL will be 4.0.
  Suppliers are encouraged to use a tighter AQL (e.g., 2.5, 1.5, 1.0) to reduce the opportunities for escapes of nonconforming parts.
If defects are found:
  The entire lot is to be quarantined and inspected 100% for conformance
  A CAR should be implemented and validated prior to removing 100% inspection from subsequent lots
  Rework done must be 100% inspected prior to release from quarantine
Next Slide
Previous Slide
Notes: Suppliers will be required to institute an AQL of 2.5 for the first five (5) production lots produced. If there is no defect(s) found after the first five (5) lots produced suppliers may ease the AQL to 4.0. If a defect is found, the entire lot will be quarantined, and 100% inspection will be required.

## Slide 20
GDLS C=0 Lot sampling chart
GDLS C=0 Lot Sampling Plan from PQA-3000
Next Slide
Previous Slide
Notes: Sampling plans must be documented and kept on file, Repeatable, and applied consistently. This slide shows the lot sampling chart that must be followed per quality clause QG5.

## Slide 21
Supplier ID Lot Verification Checklist
Used to assist in the validation of compliance for parts
SQA Regional Manager will provide direction on duration of usage
Can be found at www.gdls.com
Next Slide
Previous Slide
Notes: The supplier ID lot verification checklist may be used to assist in validation of part compliance. Think of this document as a memory jogger for new Inspection Delegates or when a supplier is experiencing a high number of escapes. The SQA regional manager will determine the duration of usage.

## Slide 22
Inspection of Part Marking
Part Marking must be inspected and verified
  If a part marking dimensional location/size is present in the TDP an actual measurement must be taken
Illegible or incorrect part marking, including non-readable IUID labels = nonconformance
Delegates must reject incorrect marking
Risks of Incorrect Part Marking
  Loss of traceability
  Assembly disruption
  Field identification issues
  Increased quality cost
Next Slide
Previous Slide
Notes: Always inspect and verify part markings as specified. Take measurements when required. Reject and document all nonconformances. Remember: Attention to part marking prevents bigger problems later. Part Marking errors are one of the most common escape types because they are treated as secondary processes. They are not. Incorrect part marking often creates downstream problems that can affect cost, late shipments, reworks, sales, similar to any other type of defect.

## Slide 23
Part Marking Requirements
Verify Part Marking per TDP:
  Permanent or non-permanent
    Test a part to confirm permanent marking is permanent
  Correct content, size and location
  Applies to detail parts, assemblies including down components in BOM
Part Marking is part of product conformity
  Part marking nonconformances will affect your Supplier Performance Scorecard
  Commercial parts may require GDLS part marking. Review TDP notes for part marking requirements.
Next Slide
Previous Slide
Notes: Always verify part marking per the TDP. Confirm permanence, check content, size, location, and review requirements for all parts and assemblies. Your attention to detail in part marking helps ensure quality and maintains supplier performance.

## Slide 24
The delegate stamp holder is responsible to assure that ALL GDLS PO & TDP requirements are satisfied by collecting data and approving requirements as applicable. Below are some examples of what could be found in the TDP
Technical Data Package (TDP) Review
Design Specifications
  Detailed design documents
  QARs/QAPs
  Specifications
  Change control documents
  Ordering Data
Material Specifications
  Certificates of Conformance
  Test reports for material used
Work Instructions
  Detailed instructions/procedures
  Test reports for material used
Corrective Action Records
  Any records of CA taken during FAI
  Variances (NCH)
Inspection and Test Records
  Documentation of all inspections and test performed including
    Methods, Results, Nonconformances noted
First Article Inspection Reports and Paperwork
  Completed GDLS Audit Record
  Completed AS9102 FAIR
  Balloon Drawing/Digital Product Definition
  ID Checklist
  Copy of PO
  Stamped Packing List
  Approval letters (weld, software, etc.)
Tooling
  Records of maintenance and Calibration for equipment used in manufacturing or inspection of parts
    All equipment performing inspection(s) for part approval(s) shall be calibrated(e.g. measuring tools, fixtures, end of line testing, etc.)
Next Slide
Previous Slide
Notes: The Technical Data Package contains all the information needed to show the part is compliant to GDLS requirements. The delegated stamp holder is responsible to assure all GDLS Purchase order & TDP requirements are satisfied. When presenting a part to a GDLS representative, all the applicable items are required to be present to gain GDLS approval. This slide contains a list of the minimal items needed during FAI review. The main categories are Design and Material specifications, Manufacturing work instructions, Inspection and Test Reports, Tooling information used for the part manufacturing and the FAI report and associated paperwork. All FAI/Source information is to be kept as records for the length of the program or per direction in your Purchase order Terms and Conditions. FAI/Source paperwork will be kept on file at the suppliers; however, the information should be made readily available to GDLS or to the government in a reasonable amount of time when requested. When completed all documentation will be signed and stamped by an appropriate supplier delegate or GDLS personnel.

## Slide 25
Technical Data Package Common Rejections
Missing or incomplete data is unacceptable
  Missing Detail FAIRs for assemblies
  Missing or out of date weld approvals
  Incomplete AS9102 forms
Part marking incorrect
  Illegible
  Incorrect location
  MRI barcodes not scanning
  Wrong part number
Any uncalibrated or past due calibrations are not acceptable
Out of tolerances conditions(without an approved NCH)
- NCH must be referenced on the PO
Non DFARS material
Next Slide
Previous Slide
Notes: These are common rejections that SQA has seen over the years. These issues can significantly impact product integrity, compliance, and customer satisfaction. Missing or incomplete data is strictly unacceptable. Part marking errors, such as incorrect information, illegible markings, or incorrect locations, cannot be tolerated. Any uncalibrated or past-due calibrations are strictly prohibited. Out-of-tolerance conditions, unless covered by an approved NCH, are not allowed. Addressing these issues is critical to maintaining our standards and ensuring compliance with industry regulations.

## Slide 26
Certificate of Conformance (CoC)
Certifications where applicable must contain the following information as a minimum:
  The heat/lot number/batch/date codes
  Applicable part number/specification and revision
  Inspection data, Chemical, Ballistic, etc. as applicable
  Signature & Date performed/tested, where applicable
  CoCs are only accepted from the manufacturer of the part or from an authorized distributor
  Certifications for protective coatings(e.g. anodizing, painting, plating) must specify:
    Class, type and/or grade to which the finished product conforms to
Certificate of Conformance review is mandatory
Note: COCs are not required to be sent with the shipment unless directed to by the PO
Next Slide
Previous Slide
Notes: This slide will review the minimum requirements for certifications and some important training notes to ensure compliance and prevent common errors. First, all certifications—where applicable—must contain the following information at a minimum: The heat, lot, batch, or date codes. The applicable part number, specification, and revision. Relevant inspection data, such as chemical or ballistic results, as applicable. Signature and date performed or tested, where required. It’s important to note that Certificates of Conformance, or C of C's, are only accepted if they come directly from the manufacturer of the part, or from an authorized distributor. For protective coatings, such as anodizing, painting, or plating, the certification must specify the class, type, and/or grade to which the finished product conforms. A thorough review of each Certificate of Conformance is mandatory. However, C of C's are not required to be sent with the shipment unless specifically directed by the purchase order. Material certification errors are a frequent cause of escapes. It’s essential that delegates confirm alignment between the certifications and the physical parts. Additionally, delegates must ensure that all special processes were performed by approved sources and are properly documented. By following these guidelines, we can help maintain compliance and avoid costly errors in our processes.

## Slide 27
Material Certifications
VS
What is the difference between these material notes and what does it mean when you’re conducting your audit?
C of C’s for material must always come from the manufacturer of the material and not a distributor.
  C of C’s may be accepted from authorized franchise distributors (AFD) if proof of being an AFD is presented.
Always purchase material in the thickness as specified.
Next Slide
Previous Slide
Notes: Be sure to order material thickness listed on the drawing. The above example details the drawing requirements, do not order thicker material and machine down. The bottom example will allow suppliers to buy material thicknesses as large as needed to produce the dimensions shown in the TDP.

## Slide 28
Discovery of Nonconforming Product
Stop shipment immediately and notify GDLS Buyer
Perform containment actions - Segregate affected product
Read across to check similar part numbers for defect
Notify your quality management
Do not ship without disposition – need an approved NCH document
Begin RCCA
Repairs CANNOT be done without prior approval from GDLS – would need NCH for approval to ship
Rework is acceptable to perform without approval from GDLS
Next Slide
Previous Slide
Notes: When a nonconforming product is identified, it’s critical to take the following immediate actions: First, stop shipment immediately and notify your GDLS Buyer. Perform containment actions by segregating all affected products to prevent further issues. Read across to check similar part numbers for the same defect—this helps prevent escapes across families of parts. Notify your quality management team right away.
Do not ship any affected product without proper disposition—this means you must have an approved NCH document before shipping. Begin the RCCA process to determine root cause and corrective actions.
Repairs cannot be performed without prior approval from GDLS; you’ll need an NCH for any repair approval and subsequent shipment. Rework, however, is acceptable to perform without GDLS approval.

## Slide 29
Know the Difference - Repair vs. Rework
REPAIR – the action of taking a nonconforming product and modifying it to make it acceptable for the parts intended use but is not 100% to the technical data package requirements
  Example(s) of Repair:
    Performing weld fill on a hole that was originally cut oversize and then drilled again to meet specification,
    Drilling and tapping holes in a part to use in a jig during machining and then weld filling those holes,
    Any/all fixture(s)/manufacturing process(es) requiring removal of parent part material would also be considered a repair
  Repairs CANNOT be done without prior approval from GDLS on an NCH document
  Any repairs done without prior approval from GDLS may be subject to scrap
REWORK – the action of taking a nonconforming product and performing the same processing or equivalent processing to bring a part within the specification of the technical data package
  Example of rework:
    Performing an additional drilling or reaming process to bring a hole into specification that was originally undersize).
  Rework is acceptable to perform without approval from GDLS
Next Slide
Previous Slide
Notes: Let’s clarify the important distinction between Repair and Rework when addressing nonconforming products: Repair involves modifying a nonconforming product to make it usable for its intended purpose, but the result does not fully meet the original technical data package requirements. It’s critical to remember: Repairs cannot be performed without prior approval from GDLS on an NCH document. Any repairs done without this prior approval may result in the part being scrapped. Rework, on the other hand, means bringing a nonconforming product back into full compliance by repeating or performing equivalent processing, so the part meets all technical data package specifications. Rework is acceptable to perform without GDLS approval.

## Slide 30
Final Shipment Authorization
Confirm:
  Product conformity
  Documentation completeness
  Traceability
  Previous GDLS FAIR approval on file to same revision
    No changes occurred since last FAIR approval
Once verification of TDP has been found compliant to PO requirements, inspection delegate can stamp the packing list and release for shipment
Next Slide
Previous Slide
Notes: Before any product is released for shipment, it’s essential to confirm the following: Product conformity – Ensure the product meets all specified requirements. Documentation completeness – All required paperwork must be accurate and complete. Traceability – Confirm that all traceability records are in order. Previous GDLS FAIR approval – Verify that there is an approved FAIR on file for the same revision. No changes since last FAIR approval – Ensure no changes have occurred since the last approved FAIR. Once you have verified that the Technical Data Package is compliant with the Purchase Order requirements, the inspection delegate may stamp the packing list and release the product for shipment. Remember, this is the final barrier before the product reaches the customer. If anything feels incomplete or incorrect, the right decision is to stop and escalate the issue immediately.

## Slide 31
Vendor Inspection Delegation Audit (VIDA)
Supplier will be subject to GDLS VIDA audit
Done on a periodic basis
  Either self led or GDLS led
Yearly training is required
To help expedite the on-site visit prepare information in advance
Performance history is distributed monthly and will need to be available for VIDA audit
Failure to complete the VIDA may result in suspension or removal of ID stamps
Successful completion of the audit will guarantee continued partnership in the ID Program
Next Slide
Previous Slide
Notes: All suppliers participating in the GDLS ID Program will be subject to a VIDA audit. These audits are conducted on a periodic basis and may be either self-led or led by GDLS. Yearly training is required for all participating suppliers. To help expedite the on-site visit, it’s important to prepare all necessary information in advance. Performance history is distributed monthly and must be available for review during the VIDA audit. Failure to complete the VIDA audit may result in suspension or removal of your ID stamps. On the other hand, successful completion of the audit will guarantee your continued partnership in the ID Program. By staying prepared and proactive, you help ensure a smooth audit process and maintain your good standing in the program.

## Slide 32
Inspection Delegate Responsibilities
Have a copy and review the GDLS or GDLS-C P.O. during the inspection
Have a copy of the GDLS or GDLS-C Print (same part # & revision level per P.O.)
Know if a previous First Article Inspection (FAI) has been completed or if a full or partial FAI is required prior to shipment
Review the GDLS Quality Clauses listed on the PO and confirm the requirements have been met (If quality clauses are in error or N/A contact your buyer for resolution)
Know if any changes have occurred in design, manufacturing process, materials, location, sub-tier supplier sources since the last FAI was approved
In-Process and Final Inspection are complete in accordance with GDLS and internal supplier requirements
Process monitoring to assure items such as settings on weld machines, work instruction compliance, cure times, etc. are followed
  Verification of items such as weld sample approval, material certifications, first article test approval, control test approval are current
  Document FAI on the GDLS FAI Forms found on our website: https://www.gdls.com
Assure all requirements of the P.O. and Print have been met
If you have questions, call your GDLS Regional SQA Manager: https://www.gdls.com
Each part number shipped under the ID program with QJ21 as a clause on the PO must have a FAIR approved by a GDLS SQA Inspector or GDLS Regional Manager prior to the Supplier’s Inspection Delegate stamping packing slips
Next Slide
Previous Slide
Notes: When preparing for inspection and First Article submission, follow these essential steps:
1. Have a copy and review the GDLS or GDLS-C Purchase Order during inspection.
2. Have a copy of the corresponding GDLS or GDLS-C print and ensure the part number and revision match the P.O.
3. Determine FAI status, Know if a previous First Article Inspection (FAI) has been completed, or if a full or partial FAI is required prior to shipment.
4. Review GDLS Quality Clauses listed on the P.O. and confirm all requirements are met. If any clauses are in error or not applicable, contact your buyer for resolution.
5. Check for changes: Confirm if any changes have occurred in design, manufacturing process, materials, location, or sub-tier supplier sources since the last approved FAI.
6. Complete in-process and final inspection per GDLS and internal supplier requirements. Monitor processes to ensure compliance with items like weld machine settings, work instructions, and cure times.
7. Verify approvals and certifications such as weld sample approval, material certifications, first article test approval, and control test approval are current.
8. Document the FAI using the GDLS FAI Forms available at www.gdls.com. Ensure all P.O. and print requirements are met before shipping. If you have questions, contact your GDLS Regional SQA Manager—contact information is available at www.gdls.com. For parts with QJ21 clause: Each part number shipped under the ID program with QJ21 on the P.O. must have a FAIR approved by a GDLS SQA Inspector or Regional Manager before the Supplier’s Inspection Delegate can stamp the packing slip. By following these steps, you help ensure compliance, reduce risk, and maintain quality in every shipment.”

## Slide 33
Inspection Delegate Stamp Rules
STAMP RULES:
This stamp will always be kept under personal control and secured from unauthorized use (stamps are not borrowed or loaned).
  The stamp is like your signature and should be with you or locked up when not in use.
Assignee must have independent authority to accept or reject product shipment(s). Must also be unencumbered from contacting their SQA Regional Manager with any questions or concerns.
Stamp use is only for its intended purpose, the review of GDLS product and documentation (a written/typed stamp number is not valid).
Immediately notify your GDLS Regional Manager if this stamp is lost, stolen, or if it cannot be used because of damage or wear.
Immediately notify your GDLS Regional Manager and GDLS Buyer if you suspect any misuse of this stamp.
The stamp impression must be affixed to all copies of the shipping documents only when compliance to the Purchase Order and TDP are fully met. This is the only form of product acceptance when received at a GDLS facility.
Next Slide
Previous Slide
Notes: Your GDLS inspection stamp is your personal signature of product acceptance. Please follow these important rules: Personal Control: Always keep your stamp under your direct control—never loan or borrow stamps. When not in use, keep your stamp locked up and secured from unauthorized access. Authority: You must have independent authority to accept or reject product shipments. You should always feel free to contact your SQA Regional Manager with any questions or concerns. Proper Use: Use the stamp only for its intended purpose: reviewing GDLS product and documentation. Handwritten or typed stamp numbers are not valid—only the actual stamp impression is acceptable.
Immediate Notification: If your stamp is lost, stolen, damaged, or unusable, notify your GDLS Regional Manager immediately. If you suspect any misuse of the stamp, notify both your GDLS Regional Manager and GDLS Buyer right away. Stamping Shipping Documents: Only affix your stamp to shipping documents when the product and documentation are fully compliant with the Purchase Order and Technical Data Package. The stamp impression is the only recognized form of product acceptance at GDLS facilities. Your diligence protects both you and the integrity of the GDLS quality process.

## Slide 34
Unwavering Commitment to Quality
REMEMBER...
EVERYTHING YOU PLAN, WRITE, PRODUCE, INSPECT MUST BE USED BY THESE SERVICE MEMBERS
THEY WILL BE THE FIRST TO PAY FOR OUR MISTAKES
Next Slide
Previous Slide
Notes: Everything we plan, write, produce, and inspect is ultimately used by our service members. They rely on our commitment to quality and attention to detail. If we make a mistake, they will be the first to pay the price.
Let’s always keep their safety and success at the forefront of everything we do.”

## Slide 35
THANK YOU!!!!
Your dedication and attention to detail in inspection efforts are essential to ensuring the quality of our products and safeguarding the lives of the brave men and women on the front lines. Every component you inspect and every standard you uphold directly contributes to the safety and reliability of the equipment our soldiers depend on.
The lives of those who defend our freedoms rest in your hands, and your commitment to excellence makes all the difference. Together, we share the responsibility of delivering nothing less than perfection.
Notes: Your dedication and attention to detail in inspection efforts are essential to ensuring the quality of our products and safeguarding the lives of the brave men and women on the front lines. Every component you inspect and every standard you uphold directly contributes to the safety and reliability of the equipment our soldiers depend on. The lives of those who defend our freedoms rest in your hands. Your commitment to excellence makes all the difference. Together, we share the responsibility of delivering nothing less than perfection.